It sounds like you're attempting to configure the CAN peripheral on the STM32F429 to operate in Loopback Mode (test mode) without external hardware connected to the `CAN_RX` and `CAN_TX` pins, but you're encountering an issue where the CAN controller remains in initialization mode (`INAK` bit stays set) even after clearing the `INRQ` bit. Let’s troubleshoot this step-by-step and provide a solution.

---

### Background on CAN Initialization and Loopback Mode
The STM32F429’s CAN peripheral (based on the Bosch CAN 2.0B specification) has several operating modes, including Initialization Mode, Normal Mode, and Test Modes (like Loopback Mode). Here’s what’s relevant:
- **Initialization Mode**: Entered by setting the `INRQ` bit in the `CAN_MCR` register. The `INAK` bit in `CAN_MSR` is set to indicate the CAN is in this mode.
- **Normal Mode**: Exited from Initialization Mode by clearing `INRQ`. The `INAK` bit should clear when the transition is successful.
- **Loopback Mode**: Enabled by setting the `LBKM` bit in the `CAN_BTR` register. In this mode, the CAN controller internally connects `CAN_TX` to `CAN_RX`, allowing self-testing without external hardware.

For the CAN peripheral to successfully exit Initialization Mode:
1. The CAN peripheral must be properly initialized (baud rate, mode settings, etc.).
2. The transition from Initialization Mode to Normal Mode (or Loopback Mode) requires specific timing and conditions to be met.

If `INAK` remains set after clearing `INRQ`, it indicates the CAN controller hasn’t successfully transitioned out of Initialization Mode.

---

### Possible Issues and Troubleshooting
Here are common reasons why the CAN might not exit Initialization Mode in your setup:

#### 1. **Improper CAN Bit Timing Configuration**
   - The `CAN_BTR` (Bit Timing Register) must be correctly configured before exiting Initialization Mode. If the baud rate prescaler, time segments (`TS1`, `TS2`), or synchronization jump width (`SJW`) are invalid, the CAN peripheral may fail to start.
   - **Check**: Ensure `CAN_BTR` is configured with valid values for your system clock and desired CAN baud rate.

#### 2. **CAN Clock Not Enabled**
   - The CAN peripheral clock must be enabled in the RCC (Reset and Clock Control) registers before it can operate.
   - **Check**: Verify that the CAN1 (or CAN2, depending on which you’re using) clock is enabled in `RCC_APB1ENR`.

#### 3. **Loopback Mode Not Properly Enabled**
   - The `LBKM` bit must be set in `CAN_BTR` while the CAN is still in Initialization Mode (i.e., before clearing `INRQ`).
   - **Check**: Confirm that `LBKM` is set in `CAN_BTR` before attempting to exit Initialization Mode.

#### 4. **Incorrect Sequence of Operations**
   - The CAN peripheral requires a specific sequence to transition from Initialization Mode to Normal Mode (or Loopback Mode). Clearing `INRQ` too early or without proper setup can cause the issue.
   - **Check**: Follow the correct initialization sequence (detailed below).

#### 5. **Missing Filter Configuration**
   - Although not strictly required for Loopback Mode, uninitialized filters can sometimes cause unexpected behavior depending on the firmware library or setup.
   - **Check**: Initialize at least one filter to accept messages (optional but good practice).

#### 6. **Hardware Pin Configuration**
   - Even in Loopback Mode, the GPIO pins for `CAN_TX` and `CAN_RX` must be configured correctly as alternate function pins for the CAN peripheral.
   - **Check**: Ensure the GPIO pins are set to alternate function mode with the correct AF number (typically AF9 for CAN1/CAN2 on STM32F429).

---

### Correct Initialization Sequence for CAN in Loopback Mode
Here’s a step-by-step guide to initialize the CAN peripheral in Loopback Mode on the STM32F429:

#### Step 1: Enable the CAN Peripheral Clock
```c
RCC->APB1ENR |= RCC_APB1ENR_CAN1EN; // Enable CAN1 clock (adjust for CAN2 if needed)
```

#### Step 2: Configure GPIO Pins
Even in Loopback Mode, the pins must be configured as alternate function pins. For example, if using CAN1 with `PA11` (CAN_RX) and `PA12` (CAN_TX):
```c
RCC->AHB1ENR |= RCC_AHB1ENR_GPIOAEN; // Enable GPIOA clock
GPIOA->MODER &= ~(GPIO_MODER_MODER11 | GPIO_MODER_MODER12); // Clear mode
GPIOA->MODER |= (GPIO_MODER_MODER11_1 | GPIO_MODER_MODER12_1); // Alternate function mode
GPIOA->AFR[1] &= ~(GPIO_AFRH_AFSEL11 | GPIO_AFRH_AFSEL12); // Clear AF selection
GPIOA->AFR[1] |= (9 << GPIO_AFRH_AFSEL11_Pos) | (9 << GPIO_AFRH_AFSEL12_Pos); // AF9 for CAN1
```

#### Step 3: Enter Initialization Mode
```c
CAN1->MCR |= CAN_MCR_INRQ; // Request initialization
while (!(CAN1->MSR & CAN_MSR_INAK)); // Wait for INAK to be set
```

#### Step 4: Configure CAN Bit Timing and Loopback Mode
Set the baud rate and enable Loopback Mode in `CAN_BTR`. Example for 500 kbps with a 42 MHz APB1 clock:
- Prescaler = 6
- TS1 = 11 (BS1 = TS1 - 1 = 10)
- TS2 = 4 (BS2 = TS2 - 1 = 3)
- SJW = 1
```c
CAN1->BTR = (0 << CAN_BTR_SILM_Pos) | // Normal mode (not silent)
        (1 << CAN_BTR_LBKM_Pos) | // Enable Loopback Mode
        (0 << CAN_BTR_SJW_Pos) | // SJW = 1 (0 + 1)
        (10 << CAN_BTR_TS1_Pos) | // TS1 = 11 (10 + 1)
        (3 << CAN_BTR_TS2_Pos) | // TS2 = 4 (3 + 1)
        (5 << CAN_BTR_BRP_Pos); // Prescaler = 6 (5 + 1)
// Baud rate = 42 MHz / (6 * (1 + 11 + 4)) = 500 kbps
```

#### Step 5: Optional - Configure Filters
Set up a basic filter to accept all messages (optional but recommended):
```c
CAN1->FMR |= CAN_FMR_FINIT; // Enter filter init mode
CAN1->FA1R &= ~CAN_FA1R_FACT0; // Deactivate filter 0
CAN1->FS1R |= CAN_FS1R_FSC0; // 32-bit scale for filter 0
CAN1->sFilterRegister[0].FR1 = 0; // Accept all IDs
CAN1->sFilterRegister[0].FR2 = 0; // Mask all bits
CAN1->FA1R |= CAN_FA1R_FACT0; // Activate filter 0
CAN1->FMR &= ~CAN_FMR_FINIT; // Exit filter init mode
```

#### Step 6: Exit Initialization Mode
```c
CAN1->MCR &= ~CAN_MCR_INRQ; // Clear INRQ to start CAN
while (CAN1->MSR & CAN_MSR_INAK); // Wait for INAK to clear
```

#### Step 7: Verify Operation
If `INAK` clears, the CAN is in Loopback Mode. You can now transmit a message and check if it’s received in the RX FIFO.

---

### Debugging Tips
If `INAK` still doesn’t clear:
1. **Check `CAN_BTR` Values**: Use a debugger to verify the exact value written to `CAN_BTR`. Incorrect timing parameters are a common culprit.
2. **Clock Source**: Ensure the APB1 clock frequency matches your calculations (e.g., 42 MHz if using HSI or PLL-derived clocks).
3. **Register Access**: Confirm you’re accessing the correct CAN peripheral (e.g., `CAN1` at `0x40006400`).
4. **Timeout**: Add a timeout to the `while (CAN1->MSR & CAN_MSR_INAK)` loop and print an error if it doesn’t clear:
   ```c
   uint32_t timeout = 1000000;
   while ((CAN1->MSR & CAN_MSR_INAK) && timeout--) {
       if (timeout == 0) {
        // Error: CAN didn’t start
        break;
       }
   }
   ```

---

### Example Full Code
```c
#include "stm32f4xx.h"

void CAN_Init(void) {
    // Enable clocks
    RCC->APB1ENR |= RCC_APB1ENR_CAN1EN;
    RCC->AHB1ENR |= RCC_AHB1ENR_GPIOAEN;

    // Configure PA11 (CAN_RX) and PA12 (CAN_TX)
    GPIOA->MODER &= ~(GPIO_MODER_MODER11 | GPIO_MODER_MODER12);
    GPIOA->MODER |= (GPIO_MODER_MODER11_1 | GPIO_MODER_MODER12_1);
    GPIOA->AFR[1] &= ~(GPIO_AFRH_AFSEL11 | GPIO_AFRH_AFSEL12);
    GPIOA->AFR[1] |= (9 << GPIO_AFRH_AFSEL11_Pos) | (9 << GPIO_AFRH_AFSEL12_Pos);

    // Enter initialization mode
    CAN1->MCR |= CAN_MCR_INRQ;
    while (!(CAN1->MSR & CAN_MSR_INAK));

    // Configure CAN for 500 kbps in Loopback Mode
    CAN1->BTR = (1 << CAN_BTR_LBKM_Pos) | (0 << CAN_BTR_SJW_Pos) |
        (10 << CAN_BTR_TS1_Pos) | (3 << CAN_BTR_TS2_Pos) | (5 << CAN_BTR_BRP_Pos);

    // Exit initialization mode
    CAN1->MCR &= ~CAN_MCR_INRQ;
    uint32_t timeout = 1000000;
    while ((CAN1->MSR & CAN_MSR_INAK) && timeout--);
    if (timeout == 0) {
        // Error handling: CAN didn’t start
    }
}

int main(void) {
    CAN_Init();
    while (1) {
        // Test CAN by sending/receiving messages
    }
}
```

---

### Conclusion
If you follow the above sequence and verify each step, the CAN peripheral should exit Initialization Mode (`INAK` clears) and enter Loopback Mode successfully. The most likely issue in your case is either an incorrect `CAN_BTR` configuration or a missing clock/GPIO setup. Let me know your current code or specific `CAN_BTR` values if you need further assistance!